## Slide 1: CAD Tools
Synopsys and Cadence

## Slide 2: ASIC Design Example
INV
NAND2
DFF
NOR2
XOR2
MUX2:1
AOI21
DFF
DFF
OAI21
INV
NOR2
XOR2
INV
Inputs
Outputs

## Slide 3: RTL – GDS FLOW
Design Specification
Behavioral Description (.v)
Logic Synthesis
Synopsys DesignVision
Synthesized Gate Level Netlist (.v)
Automatic Place and Route
Cadence Innovus
Final Design Verification (.gds/ .def)
Cadence Virtuoso
Standard Cell Library (schematic, layout, symbol, abstract)
Cadence Virtuoso
DRC/ LVS
Clean?
Library Characterization (.lib)
Synopsys PrimeLib
Library Compilation(.db)
Synopsys LC Shell
Abstract View (.lef)
No
Yes
Yes
Parasitic Extraction (.sp)
Mentor Graphics Calibre
Project 1
Project 2
Project 3
Project 4 - 5
Project 6

## Slide 4: Inverter Design Demo
Schematic
Layout

## Slide 5: Layout
Layers
  NW: n-well
  RX: Diffusion (vertical measurements of pMOS and nMOS are Wp and Wn
  respectively)
  JX: N+ source or drain implant area
  JZ: P+ source or drain implant area
  PC: Poly (horizontal measurement of PC layer is the length of the channel, L)
  CA: Contact (used to connect RX and M1, also PC and M1)
  M1: Metal 1 (used for routing inside the standard cell, VDD and GND pins are on M1)
  M2: Metal 2 (all I/O pins are on M2 layer)
  V1: Via 1 (used to connect M1 and M2)

## Slide 6: Pin Pitch and Offset
INV
NAND2
DFF
IN
OUT
A
B
OUT
Q
CLK
D
R
VDD!
VDD!
VDD!
GND!
GND!
GND!
(W/2)+(W*n)
(W)*n
(W)*n
(W)*n
(W)*n
(W)*n
(W)*n
(W)*n
(W)*n
The pin pitch should be (0.26*n), meaning it can be 0.26, 0.52, 0.78...
The offset should be (0.13 + 0.26*n), meaning it can be 0.13, 0.39, 0.65...
(W/2)+(W*n)
(W/2)+(W*n)
(W/2)+(W*n)
Pin Pitch
Offset
(W/2)+(W*n)
(W/2)+(W*n)